6.332 Final Project
2.45 GHz TLRCN Resonant Rectifier
Josh Gordonson
December 13, 2013

Introduction:

Theory:

Traditional:	-non resonant
-constant current source output filter
-excess current passes through the ZVS capacitor
-causes the diode to switch at zero volts

Typical class E zero-voltage switching (ZVS), or low dv/dt, rectifiers are designed with a discrete ZVS shunt capacitance in parallel with the diode rectifier. A large-valued LC filter makes the output look like a constant DC current source. While the diode is off, the ZVS capacitor provides a path for the mismatch in current between the input sinusoidal current source and the output current source. When the diode first turns off, the voltage across the diode and capacitor, $v_c=0$ and $\frac{dv_c}{dt}=0$. As the current through the capacitor begins to increase, the diode becomes more reverse-biased. Eventually, the current through the capacitor decreases (negative current) to the point where the voltage across the capacitor is zero again, which is when the diode begins to conduct. Since the diode switches when $\frac{dv_c}{dt}=0$, there is little power lost during the reverse recovery transient, and power dissipation during the forward transient is alleviated as well. [1] While the typical class E ZVS rectifier has nice output characteristics, its input impedance is far from resistive, due to the largely inductive output. By relaxing this constraint, Santiago-Gonzalez et al. [2] has shown that it is possible to design a class E rectifier with a near-resistive input impedance over wide power ranges.

The relaxed rectifier design is resonant, where the output inductor $L_r$ and the diode shunt capacitance $C_r$ resonate while the diode is off. $C_r$ still maintains low $\frac{dv_c}{dt}$ switching, but the input impedance is much less reactive due to the smaller-valued $L_r$. The relaxed design operates in the same way as a typical class E rectifier, but the output inductor current ripple is much larger. The current through $L_r$ resonates up while the diode is off and falls while the diode conducts.

In a typical rectifier and in Santiago-Gonzalez's work, $C_r$ is a discrete component that absorbs the diode's parasitic capacitance. In order to work at UHF and mitigate component parasitics, this work uses the diode's parasitic capacitance as $C_r$.

The ideal value of $L_r$ can be determined by following the design procedure described in Santiago-Gonzalez's paper. Starting with a diode (HBAT540B, $V_{r,peak}=33V$), resonant capacitance ($C_r=3pF$), and frequency ($f=2.45GHz$), an output voltage $V_o=7.5V$ and maximum output power $P_{o,max}=1W$ was chosen arbitrarily.
From these values, the normalized capacitance is calculated:
\begin{equation}
C_n=C_r\frac{2\pifV_o^2}{P_{o,max}}=3pF \frac{2\pi\times2.45GHz\times7.5V^2}{1W}=2.6
\end{equation}
This normalized capacitance is well off the plots provided, but extrapolating from Figure 5 in Santiago-Gonzalez et al, we find that for $C_n=2.6$, $L_n\approx0.3$, and:
\begin{equation}
L_r=L_n\frac{V_o^2}{2\pi fP_{o,max}}=1.1nH
\end{equation}

Given this, spice simulations were used to verify the results.

[image of simulation schematic]

Transient simulations were used to determine the input power, output power, efficiency, input resistance, input phase, and peak diode voltage while varying the input power, output voltage, and inductor value.
The approximated ideal inductance was off by about a factor of two, and the actual ideal inductor was found to be 2.3nH.
The ideal output voltage was found to be 9.5V.

This produced an input impedance that varied from 20-180$\omega$ over a 1W to .1W operating range with $12^/circ$ maximum phase.

Settling on these parameters, a two-stage TLRCN board was designed to compress the 20-180$\omega$ impedance down to 48-52$\omega$. The board was fabricated with additional areas to calibrate out to the reference plane and test the TLRCN and rectifier blocks. On the test bench, the isolated rectifier produced a minimum voltage standing wave ratio of 3 over the operating range. The input impedance was clearly not resistive. To determine whether or not the reactance was positive or negative, a few values of shunt capacitance and inductance were applied to the input leg. All shunt capacitors made the VSWR higher, whereas some values of shunt inductance slightly decreased the VSWR. Inferring that the input reactance was negative, a series inductor was inserted between the TLRCN and the rectifier in an attempt to cancel the negative reactance. With a 2.7nH series inductance, the VSWR dropped to a minimum of 1.8. There likely was an inductance that could have dropped the VSWR to 1, but only a small range of inductors were available, stepping over .2 or .3nH. In an attempt to tune out the reactance, a range of shunt capacitances were tested. An 0.7pF shunt capacitor resulted in a VSWR of 1.1. Success.

Relaxed:
-resonant
-diode capacitance is the resonant capacitor
-inductor discharges slowly while diode was on
-resonates up with capacitor when diode turns off

Design Procedure:
-use santiago's paper's procedure for resonant inductor
-do simulations over output voltage range and input power range
-talk about self-resonant capacitor
-build it

Starting with the diode manufacturer's device model and package parasitic data, a spice simulation was constructed for the anticipated rectifier topology (Figure /ref{top1}). The power source was simulated as a sinusoidal 2.45GHz current source, $I_1$. A number of parametric transient simulations were used to determine the values of $L_r$ and $V_o$ that produced the lowest input reactance and highest efficiency over a range of input power levels.

Initial Results:

-high VSWR
-inductive? No, tried resonating out with parallel capacitance
-capacitive? Yes, tried resonating out with parallel inductance, worked!
-series inductance added to kill negative reactance
-improvement, but not enough. (discrete inductance values limit our ability to match)
-overshoot with inductance and use shunt capacitor to improve VSWR

Reactance Canceling:

Final Results:

Analysis of Class E Zero-Voltage-Switching
Rectifier	MARIAN K. KAZIMIERCZUK
IEEE TRANSACTIONS ON CIRCUITS AND SYSTEMS, VOL. 37, NO. 6, JUNE 1990